| SECTION D GROUND-WORKS | Product and manufacturer’s details | Ability to be disassembled, reused, recycled, downcycled YY=yes, easily YH= yes, with high work input N=no U=unknown V-varies according to product | Relevant system features | Non-disassembleable / reusable / recyclable alternatives | Issues to consider | Advantages of reusable/ recyclable option | Frequency of use / examples of reuse / recycling |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Foundations | Product: pre-cast piles Main use: all types of buildings Manufacturer: Roger Bullivant www.roger-bullivant.co.uk | Reuse as new – YY Reuse 2nd hand – YY Recycling – YY Downcycle – YY | Precast concrete piles are hammered into the ground and often left insitu even after the building has been demolished. | Trench / strip foundations are virtually impossible to dig out and recycle. | Reusing or recycling pipes is unusual due to the difficulties of removing them and the lack of disadvantages of leaving them in the ground. However, if removed they would be able to be reused, subject to their integrity, or recycled to create aggregate for new piles or downcycled into hardcore. Note BRE is currently compiling information on the use of recycled aggregate, including case studies. Numerous case studies are already available on www.aggregain.org.uk | Installation is very fast and is less weather dependent and therefore economic There are no or less spoils to be removed from site. Ground works are often carried out in poor working conditions, therefore minimising this activity is desirable in terms of improving the work environment. | Common use Reuse uncommon Recycling uncommon |
|  | Product: pre-cast ground beams Main use: all types of buildings Manufacturer: Roger Bullivant www.roger-bullivant.co.uk | Reuse as new – YY Reuse 2nd hand – YY Recycling – YY Downcycle – YY | Precast concrete piles and ground beam to take any type of floor. | Trench / strip foundations are virtually impossible to dig out and recycle. | In order to reuse ground beams the sizes available have to be taken into account. The ability to recycle into new precast elements rather than downcycle into hardcore depends on the screening of the crushed concrete and the removal of metal and other contaminants. | As above | Common use Reuse uncommon Recycling common |
| Retaining walls | Product: Plastic Sheet piling Main use: bank retention schemes Manufacturer: HL Plastic Extrusions | Reuse as new – YY Reuse 2nd hand – YY Recycling – U Downcycle – YY | Installation system similar in principle to other materials | Metal sheets will rust over time making their reuse impossible. Timber will rot. Concrete retaining structures are more difficult to disassemble. | The product is made of recycled plastic. It is inert and has a long life and good potential for reuse. It is a synthetic material therefore in permanent landscaping developments natural materials are an appropriate alternative. | The product is light to transport and handle reducing health and safety risk on site. It is cheaper than steel and concrete. | Relatively new product |