| SECTION E CONCRETE | Product and manufacturer’s details | Ability to be disassembled, reused, recycled, downcycled YY=yes, easily YH= yes, with high work input N=no U=unknown V-varies according to product | Relevant system features | Non-disassembleable / reusable / recyclable alternatives | Issues to consider | Advantages of reusable/ recyclable option | Frequency of use / examples of reuse / recycling |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FORMWORK FOR IN SITU CONCRETE | Product: Reusable steel formwork | Reuse as new – YY Reuse 2nd hand – YY Recycling – YY Downcycle – NA | System designed to be reused. | Timber formwork can generally only be recycled for lower grade applications | All metal is easily recycled. Contaminants should be kept to a minimum, but do not preclude recycling. | There is a financial advantage of reusing formwork for structures with a high number of replicated elements. | Common use Common reuse Common recycling |
| PRECAST/ COMPOSITE CONCRETE FLOORS/ ROOF DECKS | Product: beam and block floors and precast concrete planks with dry finish Main use: suspended ground floors and upper floors Manufacturer: Marshalls (concrete and EPS Jetfloors) Termodeck (precast concrete hollow core slabs) termodeck@tarmac.co.uk | Reuse as new – YY Reuse 2nd hand – YY Recycling – YY Downcycle – YY | Precast concrete floors with a dry finish can be installed to avoid a screed bonded directly to the precast elements by installing a floating screed or by using an alternative (timber) finish. | Beam and block floors with a directly applied screed finish may be recycled, but are not reusable. Systems with insulating and concrete elements with a bonded screed cannot be reused and are difficult to recycle. In situ concrete floors can be recycled, but not reused. | The joints between planks are generally sealed with a cement mix, which makes the reuse of the planks difficult. Consider replacing the cement mix with compressible fillers. | Precast floors are quicker to install than insitu concrete floors and the installation is less weather dependant. Beam and block floors can enable late decisions in terms of services penetrations through floors. | Common use. Reuse and recycling increasing. |